## Slide 2: 4
Power Tools
and Equipment
Chapter

## Slide 3: Objectives
After studying this chapter, you will be able to:
List the most commonly used power tools and equipment.
Describe the uses for power tools and equipment.
Explain the advantages of one type of tool over another.
Explain safety rules that pertain to power tools and equipment.
Correctly answer ASE certification test questions that require a knowledge of power tools and equipment.

## Slide 4: Compressed-Air System
Air compressor
Air lines
Air hoses
Pressure regulator
Quick-disconnect couplings
Filter
Lubricator
(Florida Dept. of Voc. Ed.)

## Slide 5: Air Tools
Also known as pneumatic tools
  Use stored energy of compressed air for operation
Impact wrenches
  Heavy-duty air wrenches with great deal of torque
Air ratchet
  Special air wrench designed to quickly remove fasteners
Impact sockets and extensions
  Case-hardened steel to withstand extra force

## Slide 6: Air Tools (Cont.)
Air hammer or air chisel
  Use for driving and cutting operations
Blowgun
  Use to dry and clean parts washed in solvent
Air drill
  Can drill holes, grind, polish, and clean parts
    Rotary brush
    Abrasive pad
    Rotary file

## Slide 7: Electric Tools
Fixed
  Drill press
  Bench grinder
Portable
  Portable electric drill
  Rechargeable drill
  Electric impact drill

## Slide 8: Bench Grinder
Grinding, cleaning, or polishing
Safety
  Wear eye
  protection
  Use shields
  Adjust tool rest
  Do not use
  wire wheel
  on soft metal
  parts
(Snap-on Tool Corp.)

## Slide 9: Drills
Create holes in metal
and plastic parts
  Use drill bits or twist
  drills
    Bits mount in drill
    chuck
    Keyed or keyless
Portable electric drills
  Handheld drills
    Cordless

## Slide 10: Drill Press
Large floor- or bench-mounted drill
  Large holes
  Deep holes
  Many holes in several parts
(a_v_d/Shutterstock.com)

## Slide 11: Drill Press Safety
Remove key from chuck before turning on press
Secure part to be drilled with C-clamps or other holding fixtures
Use center punch
Release pressure before bit breaks through part
Oil bit as needed

## Slide 12: Hydraulic Tools
Powered by pressurized liquid
Various types
  Floor jack
  Transmission
  jack
  Engine crane
  Hydraulic
  press
(OTC/SPX Corp.)

## Slide 13: Shop Equipment
Tire changer
  Remove and replace tires on wheels
Jack stands
  Support vehicle during repairs
Engine stand
  Hold engine assembly after removal

## Slide 14: Shop Equipment (Cont.)
Cold-solvent tank
  Remove grease and oil from parts
High-pressure washer and steam cleaner
  Remove heavy deposits from outside of large assemblies
Pressure blaster
  Enclosed cabinet
  Clean rusty or corroded parts

## Slide 15: Oxyacetylene Torch
Heat, cut, weld, or braze metal parts
Use also to remove old, rusted exhaust systems
Parts
  Oxygen tank
  Acetylene tank
  Pressure regulators
  Hoses
  Handheld torch
(Sun)

## Slide 16: Welder
Uses high electric current
Creates high-power arc to melt and fuse metal
Complete proper training before use
(Sun)

## Slide 17: Soldering Gun or Soldering Iron
Join electrical wires
  Electric current heats tip and wires
  Solder, a lead-tin alloy, applied and melts
  Cools to form strong, solid connection
(Florida Dept. of Voc. Ed.)

## Slide 18: Other Shop Equipment
Battery charger
  Re-energizes “dead” or discharged battery
Droplight
  Provides portable source of light
  Anywhere additional light needed for repairs
(Florida Dept. of Voc. Ed.)

## Slide 19: Pullers
Specialized tool
Removes
  Seals
  Gears
  Pulleys
  Steering wheels
  Axles
  Other press-on parts

## Slide 20: Creepers
Allows technician to roll around and under vehicle
Stool creeper
  Allows technician to sit while working on parts near ground
(Snap-on Tool Corp.)

## Slide 21: Roll-Around Cart
Carries various tools/equipment to job area
Allows needed tools to be within reach
Saves time and effort
(Snap-on Tool Corp.)

## Slide 22: Covers
Fender covers
  Prevent vehicle damage
Seat covers
  Protect from
  dirt, oil, and
  grease

## Slide 23: Personal Computer
Laptops
Help with many tasks
  Problem
  diagnosis
  Preprogramming
  of computer chips
  Bookkeeping
  Reference to
  service literature