## Slide 2: 9
Vehicle Maintenance, Fluid Service, and Recycling
Chapter

## Slide 3: Objectives
After studying this chapter, you will be able to:
Check a car’s fluid levels.
Explain the importance of vehicle maintenance.
Locate fluid leaks.
Replace engine oil and filter.
Change automatic transmission fluid and filter.

## Slide 4: Objectives
Perform a grease job.
Inspect for general problems with hoses, belts, and other components.
Demonstrate safe practices while working with vehicle fluids.
Recycle or properly dispose of auto shop wastes.
Correctly answer ASE certification test questions on fluid service and vehicle maintenance.

## Slide 5: Vehicle Fluids
Engine oil
Coolant
Brake fluid
Transmission fluid
Power steering fluid
Other liquids

## Slide 6: Lubrication Service
Checking fluid levels and conditions
Changing engine oil and filter
Changing automatic transmission fluid
Lubricating (greasing) chassis parts constructed with grease fittings
Locating liquid leaks and other obvious problems
Following state regulations for recycling and disposal of waste fluids

## Slide 7: Vehicle Maintenance
Includes any operation that will keep vehicle in good operating condition
No proper care
  Automobile life may be reduced

## Slide 8: Fluid Service
Check service manual
  Location of all fluid checkpoints and fill points
  Interval between fluid checks and changes
  Correct type and quantity of fluids
(VW)

## Slide 9: Checking Engine Oil
Warm engine
Locate and remove dipstick
  Wipe off and replace it
  Pull dipstick back out and hold over shop rag
Oil level
  Between ADD (LOW) and FULL marks on dipstick

## Slide 10: Checking Engine Oil (Cont.)
Inspect condition of oil
  Not too thick or thin
  Not too dirty
  Does not smell like gasoline
Overfilling can cause oil foaming
  Oil absorbs air bubbles
  Reduces lubricating ability

## Slide 11: Adding Engine Oil
Obtain correct oil
  Look for lubrication sticker in engine compartment
  Use same oil as last oil change if possible
Remove oil cap
  Usually located on valve cover
Install funnel
Pour slowly

## Slide 12: Changing Engine Oil and Filter
Warm up engine
Put on eye or face protection and gloves
Raise vehicle
  Keep level
Place catch pan under oil drain plug
Unscrew drain plug
  Allow oil to drain completely
Reinstall drain plug

## Slide 13: Changing Engine Oil and Filter (Cont.)
Position catch pan under filter
  Unscrew filter using filter wrench
Obtain correct replacement filter
  Wipe small amount of oil on O-ring
Tighten by hand
  Never use filter wrench during install

## Slide 14: Changing Engine Oil and Filter (Cont.)
Lower vehicle
Add correct amount of fresh oil
Start engine and check oil pressure light
Let engine run and check for leaks
Shut off engine and check oil level again

## Slide 15: Automatic Transmission/Transaxle Fluid and Filter Service
Should be checked at specified intervals
Transmission fluid contamination
  Metal
  Dirt
  Moisture
  Friction material

## Slide 16: Checking Automatic Transmission/Transaxle Fluid
Warm up engine
Move gear selector through all positions
Apply parking brake
Place transmission in park and block wheels
With engine running, locate and remove transmission dipstick
  Some are sealed and don’t have a dipstick

## Slide 17: Checking Automatic Transmission/Transaxle Fluid (Cont.)
Wipe off dipstick and replace it
  Pull dipstick back out and hold over shop rag
Fluid level
  Between ADD (LOW) and FULL marks on dipstick

## Slide 18: Checking Automatic Transmission/Transaxle Fluid (Cont.)
Inspect fluid for discoloration and odor
  Smells burned or looks dirty, replace it
Easy to overfill transmission fluid
  Usually requires fraction of quart

## Slide 19: Changing Automatic Transmission/Transaxle Fluid and Filter
Warm up engine
Raise vehicle
Remove all but one of pan bolts
Loosen last pan bolt while holding pan
Allow pan to drop and catch fluid in catch pan
(Subaru)

## Slide 20: Changing Automatic Transmission/Transaxle Fluid and Filter (Cont.)
Replace filter
Replace and seal pan gasket
Reinstall transmission pan
Drain torque converter (if recommended)
Refill transmission fluid
  Shift through gears
  Check for leaks

## Slide 21: Manual Transmission Fluid Service
To check fluid
Locate and remove transmission fill plug
Fluid
  Warm
    Even with fill hole
  Cold
    Just below fill hole
(Chrysler)

## Slide 22: Manual Transmission Fluid Service (Cont.)
Some manufacturers suggest periodic change of manual transmission, others do not
If fluid change needed
  Remove drain plug
  Drain fluid into catch pan
  Replace drain plug
  Fill with correct fluid
  Lubricate gear shift mechanism and clutch release

## Slide 23: Differential Fluid Service
To measure fluid
Locate and remove differential fill plug
Fluid
  Hot
    Even with fill hole
  Cold
    Just below fill hole
To change fluid
Remove drain plug on bottom of differential
Use special siphon gun to draw out old fluid
(Subaru)

## Slide 24: Checking Engine Coolant
Engine coolant
  Mixture of antifreeze and water
  Must be periodically changed
  Becomes corrosive and filled with rust over time
    Damages water pump, thermostat, and radiator
To check coolant level
Look at side of overflow tank
  Between hot and cold marks
Some older cars, remove radiator cap
  1″ down in radiator

## Slide 25: Checking Power Steering Fluid
Engine off
Located in clear, plastic reservoir
  Check level to side markings
Some vehicles require removal of dipstick from power steering pump
  Check dipstick
If fluid is low, check for leaks
Replace as needed with correct fluid
Smells like burned rubber
  Flush and replace fluid

## Slide 26: Checking Brake Fluid
Inspect twice yearly
Locate master cylinder
Located in clear, plastic reservoir
  Check level to side markings
Some vehicles require removal of reservoir cover
  1/4″ down from top
Replace as needed with correct fluid

## Slide 27: Checking Fluids
Hydraulic clutch fluid
  Clutch master cylinder similar to brake master cylinder
    If low, add brake fluid
Manual steering fluid
  Check by removing fill plug or bolt from box or rack top
    Almost even with top
    If low, add recommended fluid

## Slide 28: Checking Fluids (Cont.)
Windshield washer solution
  Normally visible through storage tank
  Aids in cleaning and prevents ice formation
  Replace as needed with correct solution

## Slide 29: Checking Battery
New cars use maintenance-free batteries
Check electrolytes if needed
Clean top and terminals
  Baking soda and water

## Slide 30: Filter service
Various filters may need replacing during lubrication service
  Air filters
  Fuel filters
  Cabin filters

## Slide 31: Chassis Lubrication
Involves greasing high-friction points on vehicle
May include lubricating locks, hinges, latches, and other body parts
Grease job
  Lubrication of high-friction pivot points on suspension, steering, and drive train systems using grease gun

## Slide 32: Grease Job

## Slide 33: Body Lubrication
Engine oil
  Hard-to-reach high-friction points
Graphite
  Excellent for door and trunk locks
Dry stick (wax) lubricant
  For door latches and strikers

## Slide 34: Body Lubrication (Cont.)
Chassis grease
  Good all-around lubricant
Silicone lubricant
  Weather stripping and windows
  Canned, sprays on dry

## Slide 35: Checking Tires
Inspect tire treads
  Grooves at least 1/8″ deep
Check tire pressure
  Remove cap and check pressure with tire gauge
  Compare pressure to tire specs
  Add air if needed
  Recheck until correct

## Slide 36: Service Intervals

## Slide 37: General Inspection and Problem Location
Hose
Drive belt
Wiring
Tire
Steering system
Exhaust system
Brakes

## Slide 38: Fluid Leaks
Bad gaskets, seals, or hoses
Cracks in parts
Become familiar with different fluids
  Color
  Smell
  Feel

## Slide 39: Fluid Leaks (Cont.)
Tend to flow downward and toward rear of vehicle
Fix leaks located highest and farthest forward first
Badly soiled
  Clean area to better find source of leak
Most frequent cause of leakage is broken gaskets and worn seals

## Slide 40: Noise Detection and Location
Abnormal noises and unwanted sounds
  Knocks
  Clunks
  Rattles
  Clicks
  Hisses
  Indicate part wear or mechanical problems

## Slide 41: Noise Detection and Location (Cont.)
To pinpoint noises
Listen
Use stethoscope
Use long screwdriver
Section of vacuum hose

## Slide 42: Auto Shop Wastes
Used motor oil
Other discarded lubricants
  Transmission and differential fluids
Used parts
Cleaners and degreasers

## Slide 43: Auto Shop Wastes (Cont.)
Carburetor and injection system cleaners
Rust removers
Paint thinners
Worn out batteries
Tires and catalytic converters

## Slide 44: Auto Shop Wastes (Cont.)
Facilities that generate over 220 lb. of hazardous waste monthly
  File Uniform Hazardous Waste Manifest before removing waste
  No manifest needed for recycled materials

## Slide 45: Recycling
Some recycling materials considered hazardous waste unless destined to be recycled
  Motor oil
  Coolants
    Never mix together
Refrigerants
  Never vent into atmosphere

## Slide 46: Other Recyclables
Catalytic converters
  Contain platinum
Worn tires
  Retreading
  Shredded for road resurfacing
Batteries
  Make new batteries
Brake shoes
  Make reconditioned brake shoes

## Slide 47: Other Recyclables (Cont.)
Small assemblies (alternators, starters, master cylinders, etc.)
  Rebuilt
Plastic bumpers and body parts
  Various recycling options