## Slide 2: 23
Computer System Fundamentals
Chapter

## Slide 3: Objectives
After studying this chapter, you will be able to:
Compare computer systems to the human body’s nervous system.
Describe the input, processing, and output sections of a basic computer system.
Summarize computer system signal classifications.
Sketch a block diagram for a computer system.
Explain input sensor and output device classifications and operation.

## Slide 4: Objectives
Summarize where computers, sensors, and actuators are typically located.
Explain how a computer uses sensor inputs to determine correct outputs.
Correctly answer ASE certification test questions that require a knowledge of automotive computer system fundamentals.

## Slide 5: Computer System Fundamentals Introduction
Automotive computer
  Complex set of electronic circuits
  Produces programmed control currents for actuators after receiving input signals from sensors
Computers now monitor and control all major systems in modern vehicles

## Slide 6: Cybernetics
  Study of how electrical-mechanical devices duplicate actions of human bodies
Compares human body to computer system

## Slide 7: Cybernetics (Cont.)
Nervous system
  Computer input
Brain
  Computer processing
Reflex action
  Computer output

## Slide 8: Computer Circuit Advantages
Compensate for mechanical wear
Does not have as many mechanical parts
Can “think” very quickly
Reduce fuel consumption
Lower emissions
Increase engine power

## Slide 9: Computer Circuit Advantages (Cont.)
Reduce vehicle weight
Have on-board diagnostics
Increase driver convenience
Improve passenger safety
Compensate for component wear and failure

## Slide 10: Digital Electronics
  Studies how computer uses on-off signals to produce “artificial intelligence”
  Computers analyze input signals from sensors
  Make logical choices by comparing input signals from sensors to known signals

## Slide 11: Binary Numbering System
  Uses only two numbers, zero and one
  Key to how computers operate
Numbers zero (0) and one (1) arranged in different sequences can represent other numbers, letters, words, computer input, computer output, or conditions

## Slide 12: Gating Circuits and Truth Tables
Gate
  Electronic circuit producing specific output voltage for given input voltages
Truth table
  Shows what gate’s output will be with different inputs
  Graphically shows how gate functions
  Called logic devices because they make logical decisions

## Slide 13: Truth Tables
Two switches wired in parallel
  Either A or B (OR gate) will turn light on (output 1)
  Output will be on (1) with A or B or both energized
  Only when neither input is on will output be off (0)

## Slide 14: Gating Circuits
NOT gate or inverter gate
  Will reverse its input
  If input has voltage applied, output terminals will not have voltage or vice versa
NOT gate can be used to make other gates

## Slide 15: Gating Circuits (Cont.)
AND gate
  Requires voltage at both inputs to produce voltage
A NAND gate
  Inverted AND gate
  Output will be opposite that of AND gate

## Slide 16: Gating Circuits (Cont.)
OR gate
  Will produce output if either input is energized
NOR gate
  Inverted OR gate
  Output is inverted to produce output opposite that of OR gate

## Slide 17: Gating Circuits and Truth Tables (Cont.)

## Slide 18: Integrated Circuits
Integrated circuit (IC)
  Circuit etched on surface of tiny semiconductor chip
  Wire leads allow for connections to and from IC chip
Technicians often reprogram integrated circuits in vehicle computers to rectify problems

## Slide 19: Computer Signals
  Voltage variation over short periods of time
  Specific, arranged pulses or waves carrying electronic data, or information
Computer signals can be
  Digital
    Square or on/off scope waveform
  Analog
    Smooth, gradual change in current and voltage

## Slide 20: Computer Signals (Cont.)
Oscilloscope, or scan tool with scope function, measures computer signals
  When connected to a sensor generating signal voltage, scope displays signal trace or waveform

## Slide 21: Electrical Waveforms
AC sine wave
  Curving signal that smoothly fluctuates above and below zero volts
DC sine wave
  Curving, fluctuating signal that stays at or above zero volts
DC square wave
  Digital, on-off signal stays at or above zero volts

## Slide 22: Electrical Waveforms (Cont.)
DC ramp wave
  Moves steadily up from zero and then switches off instantly
Pulse wave
  Rises progressively from zero and then instantly returns to zero
Complex sine wave
  Moves up and down erratically but gradually

## Slide 23: Electrical Waveforms (Cont.)
Voice wave
  Irregular wave that corresponds to frequency of human voice airwaves
DC noise wave
  Straight line (dc) with some voltage fluctuations (noise)

## Slide 24: Electrical Waveforms (Cont.)

## Slide 25: Computer Signal Terminology
Pulse width or signal frequency
  Refers to how fast voltage signal changes over time
Signal amplitude
  Refers to how much voltage is present in wave
Duty cycle
  Percentage of on time compared to total cycle time

## Slide 26: Computer System Operation
Input
  Vehicle sensors convert condition into electrical signal used by computers
Processing and storage
  Computer compares inputs to data and operating parameters to determine what action to take
Output
  Electrical signals used to control physical actions and alter component operations

## Slide 27: Computer System Block Diagram
Simple service manual drawing
Shows how sensors, actuators, and computers interact
Uses basic squares or rectangles to represent components and lines to represent wires

## Slide 28: Computer System Block Diagram (Cont.)

## Slide 29: Sensors
Vehicle sensors or transducers
  Change physical condition into electrical signal
Transduce
  Means to change from one form to another
Sensors can be found almost anywhere on vehicle

## Slide 30: Sensor Classifications
Active sensor
  Produces its own voltage signal internally
Shielded wire
  Flexible metal tube around conductor to block induced voltage and interference
  Often used with active sensors
Passive sensor
  Variable resistance sensor

## Slide 31: Sensor Classifications (Cont.)
Variable resistor sensor
Switching sensor
Magnetic sensor
Hall-effect sensor
Optical sensor
Knock sensor
Solar sensor
Direction sensor

## Slide 32: Sensor Classifications (Cont.)

## Slide 33: Reference Voltage
Reference voltage (Vref)
  Base voltage used to carry computer signal
  Typically around 5 volts
Computer sends reference voltage to sensor
  Signal fed back for processing
Interpreted by computer as change in condition

## Slide 34: Reference Voltage (Cont.)

## Slide 35: Sensor Types
Intake air temperature (IAT)
Engine coolant temperature (ECT)
Oxygen (O2) sensors
Manifold absolute pressure (MAP)
Barometric pressure (BARO)
Throttle position sensor (TPS)
Fuel pressure sensor (FPS)
Engine speed sensor (ESS)
Crankshaft position sensor
Camshaft sensor (CS)

## Slide 36: Sensor Types (Cont.)
Mass airflow (MAF)
Knock sensor (KS)
Transaxle/transmission sensor
Brake switch
Wheel speed sensors
Oil level sensor
EGR sensor
Impact sensors

## Slide 37: Sensor Types (Cont.)
Vehicle speed sensor
Fuel tank pressure sensor (FTPS)
Battery temperature sensor
Computer-mounted sensors
Hybrid drive circuit sensors

## Slide 38: Circuit Sensing
Computer uses itself to monitor component and circuit operation
Circuits’ windings and wires serve as sensors

## Slide 39: Computers
Manufacturers give their computers many names
Central processing unit (CPU)
Electronic control unit (ECU)
Electronic control module (ECM)
Engine control module (ECM)
Electronic control assembly (ECA)

## Slide 40: Computers (Cont.)
Powertrain control module (PCM)
Vehicle control module (VCM)
Microprocessor
Logic module
This textbook uses ‘control module’ to refer to automotive computers in general

## Slide 41: Computer Locations

## Slide 42: Computer Types
Vehicle control module
Powertrain control module
Engine control module
Anti-lock brake module
Instrumentation module
Ignition module
Suspension system module
Climate control module
Air bag module
HV power control module
Hybrid control module
Body module

## Slide 43: Parts of a Computer
Computer housing
  Metal or plastic enclosure protecting electronic components
Circuit board
  Plastic or fiberboard insulator
  Has flat metal conductors printed on surface to connect and hold components

## Slide 44: Parts of a Computer (Cont.)
Harness connector
  Multi-pin terminal attached to vehicle’s wiring harness
Computer’s clock
  Integrated circuit with constant pulse rate to coordinate signals

## Slide 45: Parts of a Computer (Cont.)
Microprocessor
  Usually largest integrated circuit in computer
  Analyzes data from sensors
  Compares data to known good operating values in memory
Memory chips
  Store digital data

## Slide 46: Parts of a Computer (Cont.)
Voltage regulator
  Converts battery and generator voltage into lower, cleaner dc voltage usable by ECM circuits, dash displays, and sensors
Conditioners
  Also called converters or interfaces
  Alter signals for use by other chips and circuits
  Protect computer from shorted or grounded circuits

## Slide 47: Parts of a Computer (Cont.)
Buffer
  Can serve as temporary storage area for data
Microprocessor
  Means small (micro) computer (processor)
  Integrated circuit capable of analyzing data and calculating appropriate outputs

## Slide 48: Simplified Computer System

## Slide 49: Computer Memory Operation
Computer memory uses gates capable of storing data as voltage charges
Random access memory (RAM)
Read only memory (ROM)
Programmable read only memory (PROM)
Erasable programmable read only memory (EPROM)
Electrically erasable programmable read only memory (EEPROM)
Flash erasable programmable read only memory (FEPROM)

## Slide 50: KAM
Keep alive memory (KAM)
  Allows computer to use adaptive strategy
Adaptive strategy
  Needed as parts wear and components deteriorate
  Allows computer to maintain normal vehicle performance with abnormal inputs from sensors

## Slide 51: Output Drivers
Sometimes referred to as quad drivers or power transistors
Control current flow through actuators
When energized, drivers ground actuator circuits
Actuators can then produce movement

## Slide 52: Actuators
Hands and arms of computer system
Can be found almost anywhere on vehicle
Categories
  Solenoid
  Relay
  Servo motor
  Display devices
  Control module

## Slide 53: Actuator Operation
When computer turns on actuator
  It provides device with ground circuit
  Current then flows through actuator and frame ground to operate it

## Slide 54: Specific Actuators
Fuel injectors
Fuel pump
Idle air solenoid
Idle speed motor
EGR solenoids
Canister purge solenoids
Door lock motors or solenoids
Electric seat motors
Ignition coil
Ignition module

## Slide 55: Computer Networks
Series of computers that control different systems but work together to improve overall vehicle efficiency
Also called integrated computer system
Allows all on-board computers to use feedback data from several systems
Multiplexing
  Term used to describe this computer interaction in vehicles

## Slide 56: Computer Networks (Cont.)
Networked computers share common parts
  Wires
  Input signals
  Output signals
They exchange data from sensors to prevent duplication of parts and to reduce wiring
Data bus
  Wiring used for the network

## Slide 57: Serial/Parallel Network Communication
Serial communication
  Uses only one wire to exchange digital data
  Data transfers one bit at a time
Parallel communication
  Involves use of several wires
  Exchanges multiple bits of data simultaneously

## Slide 58: Serial/Parallel Network Communication (Cont.)

## Slide 59: ECM Information Flow
Star configuration
  One main processing ECM and several less complex ECMs work as a network
  Smaller ECMs cannot communicate with each other unless data is first sent through main processing ECM
Bus configuration
  Several ECMs wired to single conductor, or bus
  No main processing ECM is used

## Slide 60: ECM Information Flow (Cont.)
Ring configuration
  Each ECM wired in series, or loop
  Signal-transmitting ECM’s data flows through each ECM and then back to source ECM
  Again, no main processing ECM needed

## Slide 61: Network Wiring
Single-wire conductor
  Conventional insulated wire that carries data signals between computers
Twisted-pair conductors
  Carry computer data faster than single-wire conductors
Shielded twisted-pair conductor
  Encased in metal shield to further reduce electromagnetic interference

## Slide 62: Network Wiring (Cont.)
Differential voltage signal
  Consists of two digital signals with opposing polarities
  Synchronized to strengthen low-voltage communication signals between computers

## Slide 63: Controller Area Network
Controller area network (CAN)
  Specific type of high-speed computer data bus
  Several computers and sensors use CAN bus wiring
  Each computer is able to send and receive signals
  Each signal carries markers that denote its origin

## Slide 64: Local Interconnect Network
Local interconnect network (LIN)
  Data bus system designed to work with CAN
Suited for sensor and actuator networking applications
Used in one section such as inside a door
Special CAN-LIN bridge must be used to connect LIN to CAN system