## Slide 2: 24
On-Board Diagnostics and Scan Tools
Chapter

## Slide 3: Objectives
After studying this chapter, you will be able to:
Discuss the purpose and operation of onboard diagnostic systems.
Explain the use of scan tools to simplify reading of trouble codes.
Locate the data link connector on most makes and models of cars.

## Slide 4: Objectives
Activate on-board diagnostics and read trouble codes with a scan tool.
Erase diagnostic trouble codes.
Correctly answer ASE certification test questions concerning late-model on-board diagnostics and scan tool use.

## Slide 5: On-Board Diagnostic Systems
On-board diagnostics
  computer’s ability to analyze circuit operations, and to store and output data on any problems
Scan tool
  Communicates with vehicle computers
  Retrieves trouble codes, displays circuit and sensor values, runs tests, and gives hints for finding problems

## Slide 6: On-Board Diagnostic Systems (Cont.)
On-board diagnostics check almost every electrical/electronic part in every major system
If any abnormal values are found
  Computer stores a trouble code
  Lights malfunction indicator light on instrument panel

## Slide 7: Early On-Board Diagnostic Systems
Early systems checked limited number of items
Unable to detect weak circuits and components
Little or no standardization between systems

## Slide 8: Early On-Board Diagnostic Systems (Cont.)
OBD I systems
  On-board diagnostics generation one
  Early diagnostic systems
  Still millions of vehicles that use OBD I systems

## Slide 9: OBD II Systems
Environmental Protection Agency (EPA)
  Passed vehicle pollution laws that require on-board diagnostic systems to detect problems before they produce harmful exhaust emissions
  Standardize monitoring systems

## Slide 10: OBD II Systems (Cont.)
OBD II
  On-board diagnostics generation two
More efficiently monitor hardware and software that affect driveability emissions
Designed to keep vehicle running efficiently for at least 100,000 miles

## Slide 11: OBD II Systems (Cont.)
Greater processing speed
More memory
More complex programming
Standardized
  Data link connections
  Trouble codes
  Sensor and output device terminology
  Scan tool capabilities

## Slide 12: OBD System Comparison

## Slide 13: Malfunction Indicator Light (MIL)
In OBD II systems, engine warning light is referred to as malfunction indicator light (MIL)
If MIL glows continuously, trouble is not critical but should be repaired at owner’s convenience
MIL light comes on and then goes out
  Problem may be intermittent

## Slide 14: Malfunction Indicator Light (Cont.)
A flashing MIL
Means that trouble could damage catalytic converter and is considered critical
Trouble code chart
  Will state what each number code represents
Trouble code conversion
  Scan tool converts number code into abbreviated words

## Slide 15: Diagnostic Trouble Codes
Diagnostic trouble codes (DTC)
  Digital signals produced and stored by computer
Operating parameter
  Acceptable minimum and maximum value

## Slide 16: Computer System Problems
Loose electrical connection
Corroded electrical connection
Failed sensor
Failed actuator
Vacuum leak
Electrical short
Ignition system problems
Fuel system problems
Emission system problems
Engine problems

## Slide 17: Computer System Problems (Cont.)
Computer malfunction
Weak or lazy component
Transmission problems
Anti-lock brake system problems
Air conditioning problems
Air bag problems
Hybrid electric drive train part and circuit malfunctions

## Slide 18: Scan Tools
Retrieve trouble codes from computer’s memory and display these codes as numbers and words
Basic scan tool
  Designed to read and erase vehicle trouble codes
Advanced scan tool
    Troubleshooting guides
    More manufacturer specific tests and circuit readings

## Slide 19: Data Link Connector
Data link connector (DLC)
  Multipin terminal used to link scan tool to computer
In the past, this connector was called
  Diagnostic connector
  Assembly line diagnostic link (ALDL)

## Slide 20: Data Link Connector (Cont.)
OBD I data link connectors
  Came in various shapes and sizes
  Equipped with varying number of pins or terminals
OBD II, DLC is standardized 16-pin connector

## Slide 21: Connecting the Scan Tool
On late-model vehicles, data link connector mounts under dash
  Easily accessible from driver’s seat
In older vehicles, adapter is needed, so scan tool’s connector will fit vehicle’s pre-OBD II pin configurations

## Slide 22: Using Scan Tools
Modern scan tools give prompts in display windows
Scan tool may ask you to input VIN information
  Lets scan tool know which engine, transmission, and options are installed on that car or truck

## Slide 23: Using Scan Tools (Cont.)
(Snap-on Tool Corp.)

## Slide 24: Information a Scan Tool Can Request
Stored diagnostic trouble codes
Fault description
Datastream information
Run tests
Oxygen sensor monitoring
Failure record
Freeze frame
Troubleshooting

## Slide 25: Failure Record
Failure record or failure recorder
  Stores information on number of times trouble code occurs
OBD II systems
  Counts number of times engine reached operating temperature since last trouble code occurred

## Slide 26: Diagnostic Trouble Code Identification
OBD II requires use of set of standardized alpha-numeric trouble codes
Each trouble code identifies same problem in all vehicles, regardless of manufacturer

## Slide 27: OBD II Codes
Contain a letter and a four-digit number
Letter indicates general function of affected system
First digit indicates whether code is standard trouble code or nonuniform code

## Slide 28: OBD II Codes (Cont.)
Standard trouble codes, or SAE codes
  Indicated by zero (0)
Nonuniform codes
  Nonstandard codes assigned by manufacturers
  One (1) after system
Second digit indicates specific system function where fault is located

## Slide 29: OBD II Codes (Cont.)
Code’s last two digits
  Refer to specific fault designation
  Pinpoint exactly which component or circuit of system might be at fault and problem type

## Slide 30: OBD II Codes (Cont.)

## Slide 31: Failure Types
Hard failure
  Problem that is always present in a computer system
    Disconnected wire
Soft failure or intermittent failure
  Problem only occurs under certain conditions

## Slide 32: Computer System Failure Types
General circuit failure
Low-input failure
High-input failure
Improper range/performance failure

## Slide 33: Datastream Values
Datastream values or diagnostic scan values
  Produced by vehicle’s computer
  Give electrical operating values of sensors, actuators, and circuits
  Values can be read on scan tool’s digital display
  Compared to known normal values in service manual

## Slide 34: Key-On/Engine-Off Diagnostics
Performed by triggering ECM’s on-board diagnostic system with ignition key in on position but without engine running
Allows access to any stored trouble codes
Usually performed before key-on/engine-on diagnostics

## Slide 35: Wiggle Test
Wiggle test or “flex” test
Many computer system failures, especially intermittent failures, caused by loose, dirty, or corroded connections
If engine operation changes suddenly when connector or wire is flexed, problem located at or near that point

## Slide 36: Key-On/Engine-On Diagnostics
Performed with engine running at full operating temperature
Check condition of sensors, actuators, computer, and wiring while operating under normal conditions

## Slide 37: Switch Diagnostic Test
Involves activating various switches while using scan tool
  To instruct which switch to move and monitor operation
  Quickly indicate if switch works normally

## Slide 38: Actuator Diagnostic Test
Uses scan tool to order vehicle’s computer to energize specific output devices with engine on or off
Lets you find out if actuators work
Actuator diagnostic tests considered intrusive tests

## Slide 39: Actuator Diagnostic Test (Cont.)
Actuator diagnostic tests might
  Fire or prevent firing of ignition coil
  Open and close fuel injectors
  Cycle idle speed motor or solenoid
  Energize digital EGR valve solenoids
Scan tool will give readouts showing whether there is trouble with any actuators

## Slide 40: Scanning during a Test-Drive
With a scan tool
  Check for problems while driving vehicle
  Simulate conditions present when trouble happens

## Slide 41: Erasing Trouble Codes
Erasing trouble codes or clearing diagnostic codes
  Clears stored codes from computer memory after system repairs have been made
In most cases, codes automatically erase after 30–50 engine starts or warm-ups

## Slide 42: Erasing Trouble Codes (Cont.)
Various methods used to erase trouble codes
Use a scan tool
Disconnect battery ground cable or strap
Unplug fuse to ECM