## Slide 2: 47
Cooling System Technology
Chapter

## Slide 3: Objectives
After studying this chapter, you will be able to:
Summarize the functions of engine, supercharger, turbocharger, DEFI, and HV (hybrid vehicle) cooling systems.
Explain the operation and construction of major cooling system components found in modern vehicles.
Compare cooling system design variations.

## Slide 4: Objectives
Explain the function of antifreeze.
Identify safety procedures to follow when working with any engine, supercharger, HV motor-generator, HV battery, HV transmission, or HV engine control module.
Compare hybrid air and liquid cooling systems.
Correctly answer ASE certification test questions on cooling systems found in modern passenger vehicles.

## Slide 5: Vehicle Cooling Systems
Modern passenger vehicles can have several cooling system types
Designed to control operating temperatures of mechanical and electrical assemblies

## Slide 6: Vehicle Cooling Systems (Cont.)
Many assemblies generate internal heat during operation
  Internal combustion engine
  Supercharger
  Turbocharger
  HV battery
  Hybrid drive motor-generator
Without properly operating cooling systems, engines “self-destruct” in minutes

## Slide 7: Specific Cooling Systems
Engine cooling system
  Controls operating temperature of cylinder heads and cylinder block
Supercharger cooling system
  Must keep blower intercooler temperature cooler than engine’s operating temperature

## Slide 8: Specific Cooling Systems (Cont.)
Turbocharger cooling system
  Forces coolant through turbo bearing housing to keep turbo from overheating under prolonged high boost
HV battery cooling system
  Air or liquid removes battery cell heat when under prolonged high amperage draw

## Slide 9: Specific Cooling Systems (Cont.)
HV motor-generator cooling system
  Liquid coolant prevents motor-generator overheating in full-electric and hybrid gas-electric vehicles
HV engine control module cooling system
  Forces air or liquid through or over aluminum heat sink surrounding high-power transistors for each leg of three-phase

## Slide 10: Cooling System
(Mazda)

## Slide 11: Cooling System Functions
Removes excess heat from engine
Maintains constant engine operating temperature
Helps cold engine quickly reach operating temperature
Provides heat for passenger compartment

## Slide 12: Removing Engine Heat
Some combustion heat flows out with exhaust gas or flows into engine’s metal parts
If not removed, excess heat will seriously damage engine in minutes
Combustion flame temperature can reach 4500°F

## Slide 13: Maintaining Operating Temperature
Engine operating temperature
  Temperature engine coolant reaches under normal running conditions
  Between 180°F and 210°F
  Engine parts expand at operating temperature
  Ensures correct part clearances

## Slide 14: Reaching Operating Temperature Quickly
Engine must warm up rapidly to prevent poor combustion
Cold engine suffers from several problems
  Aluminum pistons will not be expanded by heat
    Causes too much clearance between pistons and cylinder walls
Oil in cold engine will be very thick
  Reduces lubrication and increases engine wear

## Slide 15: Heater Operation
Cooling system commonly circulates coolant to heater
Heater core
  Small liquid-to-air heat exchanger mounted under dash in passenger compartment
  Since engine coolant is warm, it can warm passenger compartment

## Slide 16: Cooling System Types
Air cooling system
  Large cylinder cooling fins and outside air remove excess heat from engine
  Shroud (routes air over cylinder fins)
Liquid cooling system
  Circulates coolant through water jackets in engine’s cylinder block and cylinder head
(Robert Bosch)

## Slide 17: Liquid Cooling Systems
Several advantages over air cooling systems
More precise control of engine operating temperature
Less temperature variation inside engine
Reduced exhaust emissions due to better temperature control
Improved heater operation to warm passengers

## Slide 18: Conventional- and Reverse-Flow Cooling
Conventional-flow cooling
  Hot coolant flows from cylinder head to radiator
  Once cooled in radiator, coolant flows back into engine block
Reverse-flow cooling
  Follows opposite course
  Cool coolant enters head and hot coolant exits block back to radiator

## Slide 19: Closed Cooling System
Uses expansion tank, or reservoir, and radiator cap with pressure and vacuum valves
Overflow tube routed into bottom of reservoir tank
Pressure and vacuum valve action pull coolant in and out of reservoir tank as needed
This keeps cooling system correctly filled at all times

## Slide 20: Open Cooling System
Does not use coolant reservoir
Overflow tube allows excess coolant to leak onto ground
Does not provide means of adding fluid automatically
No longer used on automobiles

## Slide 21: Cooling System Parts
Basic parts of engine cooling system
Water pump
Radiator hoses
Radiator
Fan
Thermostat

## Slide 22: Water Pump
Impeller
Shaft
Water pump seal
Water pump bearings
Pump hub
Pump housing
Pump gasket
(Chrysler)

## Slide 23: Water Pump Operation
Spinning engine crankshaft pulley causes drive belt to turn water pump pulley, pump shaft, and impeller
Coolant trapped between impeller blades is thrown outward by centrifugal force
Electric water pump
  Large dc motor and impeller force coolant through water jackets or through HV cooling system

## Slide 24: Radiator and Heater Hoses
Radiator hoses carry coolant between engine water jackets and radiator
Molded hose
  Manufactured in a special shape with bends to clear cooling fan and other parts
  Must be purchased to fit exact year and make of car

## Slide 25: Radiator and Heater Hoses (Cont.)
Flexible hose
  Accordion shape that can be bent to different angles
Hose spring
  Frequently used in lower radiator hose to prevent collapsing
Heater hoses
  Small-diameter hoses that carry coolant to heater core

## Slide 26: Radiator and Heater Hoses (Cont.)
Hose clamps
  Hold radiator hoses and heater hoses on their fittings
Worm-drive hose clamp
  Uses worm gear that engages slots in clamp strap to allow tightening around hose
  Most common type of replacement hose clamp

## Slide 27: Radiator
Radiator core
  Fragile center section of radiator made up of tubes and cooling fins soldered or bonded together
Radiator tanks
  Metal or plastic ends fit over core tube ends to provide storage for coolant and fittings for hoses

## Slide 28: Radiator (Cont.)
Radiator filler neck
  Opening for adding coolant that also holds removable radiator pressure cap
Transmission oil cooler
  Inner tank for cooling automatic transmission or transaxle fluid
Radiator petcock
  Fits on bottom of tank for draining coolant

## Slide 29: Radiator (Cont.)
Radiator cap
  Pressurizes water and antifreeze solution so it does not boil when operating above 212°F
Downflow radiator
  On top and bottom of core
  Core tubes run vertically between tanks
Crossflow radiator
  Modern design with tanks on sides of core
  Core tubes arranged for horizontal coolant flow

## Slide 30: Major Parts of a Radiator

## Slide 31: Types of Radiators
(Chrysler)

## Slide 32: Transmission Oil Cooler
Often placed in radiator on cars with automatic transmissions or transaxles to prevent transmission fluid from overheating
Small tank enclosed in one of main radiator tanks
Removes heat from fluid as it passes through radiator and cooler

## Slide 33: Radiator Cap
Seals top of radiator filler neck to prevent leakage
Pressurizes system to raise boiling point of coolant
  Keeps coolant from boiling and turning to steam
Relieves excess pressure to protect against system damage
In closed systems, it allows coolant flow between radiator and coolant reservoir

## Slide 34: Radiator Cap (Cont.)
Radiator cap pressure valve
  Spring-loaded disk that contacts filler neck
  Spring pushes valve into neck to form a seal
Radiator cap vacuum valve
  Opens to allow flow back into radiator when coolant temperature drops after engine operation

## Slide 35: Cooling System Fans
Pulls air through radiator core and over engine to remove heat
Engine-powered fan
  Bolts to water pump hub and pulley
  Sometimes, a fan spacer fits between fan and pulley to move fan closer to radiator

## Slide 36: Cooling System Fans (Cont.)
Flex fan
  Thin, flexible blades that alter airflow with engine speed
Fluid coupling fan clutch
  Designed to slip at higher engine speeds
  Performs same function as flexible fan
Thermostatic fan clutch
  Temperature sensitive, bimetal spring that controls fan action

## Slide 37: Cooling System Fans (Cont.)
Electric cooling fan
  Electric motor, coolant temperature sensor, and engine ECM to provide airflow and heat transfer out of radiator
Fan motor
  Small dc motor with brushes
  Mounts on bracket secured to radiator

## Slide 38: Cooling System Fans (Cont.)
Fan switch or thermo switch
  Temperature-sensitive switch that controls fan motor operation
Coolant temperature sensor
  Sensor, fuse box relays, and engine ECM operate cooling fan motors by using temperature sensor in radiator

## Slide 39: Radiator Shroud
Helps ensure that fan pulls air through radiator
Fastens to rear of radiator and surrounds area around fan
Results in huge volume of air flowing through (not around) radiator core

## Slide 40: Thermostat
Expands and contracts with changes in engine temperature
Controls coolant flow through radiator
Reduces coolant flow when engine is cold
Increases coolant flow when engine is hot
(Gates)

## Slide 41: Thermostat (Cont.)
Thermostat rating
  Stamped on thermostat to indicate its operating (opening) temperature
High thermostat heat ranges are used because they reduce exhaust emissions and increase combustion efficiency

## Slide 42: Thermostat Operation
(Chrysler)

## Slide 43: Thermostat Operation (Cont.)
Bypass valve and bypass hose, or passage
  Permit coolant circulation through engine when thermostat is closed
  If coolant cannot circulate, hot spots develop inside engine
Bypass thermostat
  Has second valve for routing hot coolant through radiator

## Slide 44: Temperature Warning Light
Informs driver when engine is overheating
When coolant becomes too hot
Temperature sending unit is closed
When engine is cold or at normal operating temperature
Temperature sending unit is open
In many late-model vehicles
Engine temperature warning light is energized by engine control module

## Slide 45: Engine Temperature Gauge
Shows exact operating temperature of engine coolant
As engine temperature increases
  Resistance drops in sending unit
  Current increases in gauge circuit
  Causes gauge needle to deflect to right, showing engine temperature

## Slide 46: Antifreeze
Mixes with water to produce engine coolant
Usually ethylene glycol
Prevents winter freeze up
Prevents rust and corrosion
Lubricates water pump
Cools engine

## Slide 47: Antifreeze/Water Mixture
50/50 mixture of water and antifreeze usually recommended
Equal mix of glycol antifreeze and water provides protection from ice formation to about –34°F

## Slide 48: Block Heater
May be used on engine to help with starting in cold weather by heating coolant
Most commonly used on diesel engines
120-volt heating element mounted in block water jacket

## Slide 49: Supercharger Cooling Systems
Uses its own electric water pump, hoses, and radiator to pump cool antifreeze through supercharger intercooler
  Air-to-liquid heat exchanger (radiator) mounted under or at outlet of compressor rotors

## Slide 50: Supercharger Cooling Systems (Cont.)

## Slide 51: Hybrid Cooling Systems
Either circulated air or circulated liquid coolant remove excess heat from components in electric powertrain
Hybrid air cooling system
  Electric blower fan and system of ducts route cool passenger compartment air around high-voltage battery pack

## Slide 52: Hybrid Cooling Systems (Cont.)
Hybrid liquid cooling system
  Electric water pump, small diameter hoses, and separate radiator or heat exchanger pull heat out of HV battery, HV PCM, and motor-generator

## Slide 53: Hybrid Cooling Systems (Cont.)
High temperatures develop in several areas within hybrid’s electric powertrain
  HV battery cells
  HV motor-generator
  HV PCM

## Slide 54: HV Battery Cooling Systems
HV battery radiator or small air-to-liquid heat exchanger mounted in battery housing
HV battery fan
  Energized by HV ECM to force fresh air through air-to-liquid heat exchanger and over battery pack outer surfaces for cooling

## Slide 55: Motor-Generator Cooling Systems
Motor-generator water jackets
  Carry liquid coolant
  Formed or machined inside stator housing during manufacture
Motor-generator coolant hoses
  Carry cooled coolant to, and heated coolant from, motor-generator water jackets

## Slide 56: Motor-Generator Cooling Systems (Cont.)
Motor-generator coolant fittings
  Allow rubber hoses to be clamped around hose for leak-proof antifreeze connections
Motor-generator water pump
  Electric coolant pump mounted between system radiator and stator housing

## Slide 57: HV PCM Cooling Systems
Often uses same electric water pump and circulated liquid coolant as motor-generator and HV battery
HV PCM water jacket
  Formed between inner and outer housings that surround high-power, control circuit boards mounted on heat sink

## Slide 58: HV PCM Cooling Systems (Cont.)
(Toyota)

## Slide 59: Coolant Heat Storage System
Needed to help keep hybrid’s piston engine warm when not running and vehicle is in full electric propulsion
Required on gasoline engine hybrids equipped with port fuel injection