## Slide 2: 73
Tire, Wheel, and Wheel Bearing Fundamentals
Chapter

## Slide 3: Objectives
After studying this chapter, you will be able to:
Identify the parts of a tire and wheel assembly.
Describe different methods of tire construction.
Explain types and sizes of tires.
Describe tire ratings and designations.
Describe different types of wheels.

## Slide 4: Objectives
Define valve stems, valve cores, lug nuts, lug studs, and lug bolts.
Identify the parts of driving and nondriving hub and wheel bearing assemblies.
Correctly answer ASE certification test questions requiring a knowledge of tires, wheels, hubs, and wheel bearings.

## Slide 5: Tires
Automobile tires perform two basic functions
  Act as soft cushion between road and metal wheel
  Provide adequate traction with road surface
Today’s automotive tires are pneumatic, or filled with air

## Slide 6: Tires (Cont.)
Today’s vehicles use tubeless tires, which have no separate inner tube
  Tire and wheel form airtight unit
Older vehicles used inner tubes
  Soft, thin, leakproof rubber liners that fit inside tire and wheel assemblies

## Slide 7: Parts of a Tire
Even with several designs, all tires have same basic parts
Beads
  Two rings made of steel wire encased in rubber
  Hold tire sidewalls snugly against wheel rim
Body plies
  Rubberized fabric and cords wrapped around beads
  Form carcass, or body, of tire

## Slide 8: Parts of a Tire (Cont.)
Tread
  Outer surface of tire that contacts road
Sidewall
  Outer part of tire that extends from bead to tread
  Markings on sidewall provide information about tire

## Slide 9: Parts of a Tire (Cont.)
Belts
  Strengthen body plies and stiffen tread
  Lie between tread and plies
Liner
  Thin layer of rubber bonded to inside of plies
  Provides leakproof membrane for modern tubeless tire

## Slide 10: Tire Construction
Many construction and design variations in tires
  Different number of plies may be used
  Plies may run at different angles
  Different materials may be used
Rolling resistance
  Measurement of friction produced as tire operates on road surface

## Slide 11: Bias Ply Tire
Plies run at angle from bead to bead
Angle reverses from ply to ply
Tread bonds directly to top ply
(Firestone)

## Slide 12: Belted Bias Tire
Bias ply tire with belts added to increase tread stiffness
Plies and belts normally run at different angles
Belts do not run around to sidewalls
  They lie under tread area only
(Firestone)

## Slide 13: Radial Ply Tire
Plies running straight across from bead to bead, with stabilizer belts directly beneath tread
Very flexible sidewall and stiff tread for very stable footprint
  Shape and amount of tread touching road surface
(Firestone)

## Slide 14: Tire Markings
Tire markings on its sidewall give information
  Tire size
  Tire model
  Load-carrying ability
  Inflation pressure
  Number of plies
  Speed rating
  Manufacturer

## Slide 15: Tire Markings (Cont.)

## Slide 16: Tire Size
Given on sidewall as letter-number sequence
Two common size designations
  Alpha-numeric and P-metric
P-metric
  Size designation is newest tire identification system
  It uses metric values and international standards

## Slide 17: Tire Size (Cont.)
Alpha-numeric
  Tire size designation uses letters and numbers to denote tire size in inches and its load-carrying capacity in pounds
Points of measure for tire are shown on right
(B.F. Goodrich)

## Slide 18: Tire Size (Cont.)

## Slide 19: Aspect Ratio
Height-to-width ratio
As number becomes smaller, tire becomes more squat
  Wider and shorter
Aspect ratio compares tire’s height and width

## Slide 20: Aspect Ratio (Cont.)
70-series tire, for example, has aspect ratio of 70
Height of tire is 70 percent of width
60 series tire would be “short” and “fat”
78 tire would be “narrow” and “tall”

## Slide 21: Maximum Load Rating
Indicates weight tire can carry at recommended inflation pressure
Printed on sidewall
P-metric ratings given in kilograms and pounds
Alpha-numeric load rating indicated by letter
  Most are load range B.
  C or D have greater load carrying ability

## Slide 22: Maximum Inflation Pressure
Maximum inflation pressure
  Highest air pressure that should be pumped into tire
Most have maximum recommended inflation pressure of 32 psi
Tires with higher load ranges can hold higher pressures and carry more weight

## Slide 23: Tread Plies
Plies and ply ratings shown on sidewall
Tire may be 2-ply tire, 2-ply with 4-ply rating, or 4-ply tire
Greater number of plies or higher ply rating generally indicate greater load-carrying ability
Number of sidewall plies also shown on tire sidewall

## Slide 24: DOT Serial Number
DOT stands for Department Of Transportation
  “DOT” on tire sidewall indicates tire passed prescribed safety tests
Following letters DOT is DOT serial number
  Identifies particular tire manufacturer, plant location, construction, and date of manufacture
DOT serial number stamped into tire sidewall

## Slide 25: Tire Grades
Tread wear
  Ratings range from 100 to 500
  Tires with higher numbers = more resistant to wear
Tire traction
  A, B, or C rating with “A” providing most traction “C” providing least
Tire temperature resistance
  A, B, or C rating, “A” resists temperature buildup better than “B” or “C” tires

## Slide 26: Speed Rating
Tire speed rating
  Maximum allowable sustained road speed a tire can safely withstand without failure
Range from B (31 mph) to Z (149 mph)
Tire’s speed rating of tire must be higher than speed at which vehicle will be driven

## Slide 27: Special Tires and Tire Features
Be familiar with several types of special tires and tire features
Compact spare tires
Self-sealing tires
Retreads
Run-flat tires

## Slide 28: Asymmetric Tires
Different tread pattern on inner edge than outer edge
Outer tread pattern designed to improve cornering on dry surfaces
Inner tread pattern designed to improve traction on wet surfaces

## Slide 29: Directional Tires
High-performance tires designed to rotate in specific direction to minimize hydroplaning
Hydroplaning
  Loss of control that occurs when layer of water prevents tire tread from contacting road surface
Directional tires have arrow and the word rotation molded onto sidewalls

## Slide 30: Spare Tires
Spare tire or spare
  Extra wheel and tire assembly that can be installed in case of flat tire
Full-size spare
  Tire of same size and type used on other four wheels of vehicle
  Can be mounted and used like any other tire
Compact or space saver spare
  Much smaller than normal tire used on vehicle
  Saves space in trunk or storage area

## Slide 31: Spare Tires (Cont.)
High-pressure spare
  Compact spare tire that holds higher-than-normal air pressure
  About 60 psi
Lightweight spare tire
  Very thin sidewall and tread construction
  Driving range and maximum speed rating are generally lower than compact spare

## Slide 32: Self-Sealing Tires
Have coating of sealing compound applied to liners
When punctuated, air pressure pushes soft compound into hole to stop air leakage

## Slide 33: Retreads
Used tires with new tread vulcanized to old carcass, or body
Retreads, also called recaps, seldom used on passenger cars
Large truck tires frequently recapped because of high cost of new tires

## Slide 34: Run-Flat Tires
Are still usable with loss of air pressure
If tire leaks, you can drive vehicle to repair shop without tire and wheel damage
Tire uses special rubber compound and thick rubber sidewall support insert that helps support weight of vehicle

## Slide 35: Wear Bars
Indicate critical amount of tread wear
Tell customer and technician that tire replacement is needed
(Goodyear)

## Slide 36: Tire Pressure Monitoring Systems
Alert driver if one or more tires are underinflated
Direct tire pressure monitoring systems
  Use pressure sensor/transmitter mounted at each wheel
  Sensors are attached to tire valves or held to wheel with metal or plastic strap

## Slide 37: Tire Pressure Monitoring Systems (Cont.)
(Toyota)

## Slide 38: Tire Pressure Monitoring Systems (Cont.)
Indirect tire pressure monitoring system
  Anti-lock brake system components monitor tire pressure
  When pressure in tire drops, tire’s circumference is reduced
  This causes wheel and tire assembly to spin faster than other tires
  Computer interprets speed sensor signal and triggers warning light

## Slide 39: Wheels
Designed to support tire while withstanding loads from acceleration, braking, and cornering
Mag wheels, or mags
  Nickname for aluminum or magnesium wheels
  These wheels do not need wheel covers
Drop-center wheel
  Commonly used on passenger vehicles
  Allows for easier installation and removal of tire

## Slide 40: Wheels (Cont.)
Outer lip that contacts tire bead
Spider
  Center section that bolts to vehicle hub
Normally, spider is welded to rim

## Slide 41: Safety Rims
Has small ridges that hold tire beads on wheel during tire blowout or flat
Blowout
  Instant rupture and air loss
Flat
  Slow leak reduces inflation pressure
(Chrysler)

## Slide 42: Valve Stems and Cores
Valve stem
  Pressed into hole in wheel of tubeless tire to allow inflation and deflation
Valve core
  Spring-loaded air valve threaded into valve stem
  Allows air to be added to tire when air chuck is placed over valve stem

## Slide 43: Valve Stems and Cores (Cont.)
Air chuck
  Tool for filling tire with air
Valve stem cap
  Screws over threaded valve stem to protect air valve and stem threads from dirt, moisture, and damage
  Prevents accidental depression of valve and resulting loss of air pressure

## Slide 44: Lug Nuts, Studs, and Bolts
Lug nuts
  Hold wheel and tire assembly on vehicle
  They fasten to special studs
Lug studs
  Special studs that accept lug nuts
  Studs are pressed through back of hub or axle flange

## Slide 45: Lug Nuts, Studs, and Bolts (Cont.)
Lug nuts and studs normally have right-hand threads (turn clockwise to tighten)
Left-hand threads will be marked with “L”
Metric threads will be identified with “M” or word “Metric”
A few cars use lug bolts instead of lug nuts
  Bolts screw into threaded holes in hub or axle flange

## Slide 46: Lug Nuts, Studs, and Bolts (Cont.)

## Slide 47: Wheel Weights
Small lead weights attached to wheel rim to balance wheel-and-tire assembly, preventing vibration
Weights offset a heavy area of wheel and tire
Aluminum wheels require stick-on lead weights with adhesive backing

## Slide 48: Hub and Wheel Bearing Assemblies
Wheel bearings
  Allow wheel to turn freely around spindle, in steering knuckle, or in bearing support
Two basic assembly designs
  Tapered roller bearing assemblies
  Ball or straight roller bearing assemblies
Wheel bearings are lubricated with heavy, high-temperature grease

## Slide 49: Hub and Wheel Bearing Assemblies (Cont.)
(Federal Mogul)

## Slide 50: Hub and Wheel Bearing Assemblies (Cont.)
Basic parts of wheel bearing
Outer race
  Steel cup or cone pressed into hub, steering knuckle, or bearing support
Balls or rollers
  Antifriction elements between inner and outer races
Inner race
  Another steel cup or cone that rests on spindle or drive axle shaft

## Slide 51: Hub and Wheel Bearing Assembly: Tapered Roller Bearings
Basic parts of hub and tapered roller bearing assembly for non-driving wheels include
Spindle
  Stationary shaft extending outward from steering knuckle or suspension system
Wheel bearings
  Tapered roller bearings mounted on spindle and in wheel hub

## Slide 52: Hub and Wheel Bearing Assembly: Tapered Roller Bearings (Cont.)
Hub
  Outer housing that holds brake disc or drum, front wheel, grease, and wheel bearings
Grease seal
  Prevents loss of lubricant from inner end of spindle and hub
Safety washer
  Flat washer that keeps outer wheel bearing from rubbing on and turning adjusting nut

## Slide 53: Hub and Wheel Bearing Assembly: Tapered Roller Bearings (Cont.)
Spindle adjusting nut
  Threaded on end of spindle for adjusting wheel bearing
Nut lock
  Thin, slotted nut that fits over spindle adjusting nut
Cotter pin
  Fits through hole in spindle, adjusting nut, and nut to lock to keep adjusting nut from turning in service
Dust cap
  Metal cap that fits over outer end of hub to keep grease in and road dirt out of bearings

## Slide 54: Hub and Wheel Bearing Assembly: Tapered Roller Bearings (Cont.)
(Chrysler, Florida Dept. of Voc. Ed.)

## Slide 55: Hub and Wheel Bearing Assembly: Ball or Straight Roller Bearings
Basic parts found in hub and wheel bearing assembly for driving wheel of front-wheel-drive vehicle
Outer drive axle
  Stub axle shaft that extends through bearings and splines to hub
Ball bearings
  Antifriction elements that allow drive axle to turn in steering knuckle or bearing support

## Slide 56: Hub and Wheel Bearing Assembly: Ball or Straight Roller Bearings (Cont.)
Steering knuckle or bearing support
  Steering or suspension component that holds wheel bearings, axle stub shaft, and hub
Driving hub
  Mounting surface for wheel
  Transfers driving power from stub axle to wheel
Axle washer
  Special washer that fits between hub and locknut

## Slide 57: Hub and Wheel Bearing Assembly: Ball or Straight Roller Bearings (Cont.)
Hub or axle locknut
  Screws on end of drive axle stub shaft to secure hub and other parts of assembly
Grease seal
Prevents lubricant loss between inside of axle and knuckle or bearing support

## Slide 58: Hub and Wheel Bearing Assembly: Ball or Straight Roller Bearings (Cont.)
(Honda)

## Slide 59: Other Hub and Wheel Bearing Assemblies
Modern vehicles use wide variation of hub and wheel bearing assemblies
Many late-model vehicles use sealed hub and bearing assembly that contains ball bearings, straight roller bearings, or tapered roller bearings
These self-contained units are not serviceable